## Slide 1
Robust Multiple Car Tracking
with occlusion reasoning
Presenter: Mohammad Shirazi
Advisor : Dr. Morris
University of Nevada, Las Vegas
Koller, Weber, Malik
University of California, Berkeley

## Slide 2
Introduction
Motion Segmentation
The Affine Motion Model
Contour Extraction & Shape Estimation
Recursive Shape Estimation & Motion Estimation
Occlusion Reasoning
Results with real world Traffic Scenes
Conclusion
Outline

## Slide 3
Idea of vision-based vehicle tracking
  Stationary cameras mounted at a location high above the road
  Having system to automatically generate traffic information like vehicle count, speed, lane change and so fourth
Advantageous
  Flexibility
  Easy Installation
  Cheap
Introduction

## Slide 4: Introduction
Vision-based tracking is always challenging
  Lights, Shadow, Noise
  Objects do not have same characteristic over different frames
  Different situation might happen like occlusion
There is need for a simple and fast but robust tracker
Perform tracking without any priori knowledge about the shape of moving object

## Slide 5
Tracking Examples
  https://www.youtube.com/watch?v=tbHWvPWhVh8
  https://www.youtube.com/watch?v=SfGAnbyjoGw
  https://www.youtube.com/watch?v=1Hpljc10gVM&NR=1&feature=fvwp
Introduction

## Slide 6
Figure 1: A block scheme of the complete tracker

## Slide 7
Motion Segmentation
Differencing between each new frame and an estimate of the stationary background
Background evolves over time
  lighting conditions change
Background is updated via the update equation
  = )+)
  is estimate of the background model, and represent rate of change of background
  is difference between frame and background
  is binary moving objects hypothesis mask
Background is updated in kalman filter formalism

## Slide 8
Motion Segmentation
The hypothesis mask, identify moving objects
Linear filters are used to increase the accuracy of the decision process
  Three filters are used for each frame (Gaussian, Gaussian derivative along the horizontal and vertical)

## Slide 9
Figure 2: block diagram of segmentation and background update procedure
Figure 3: Plot of the number of pixels correctly labeled minus incorrectly labeled
as function of added noise

## Slide 10
Figure 4: Original image (upper image) and motion hypothesis images produced by
an intensity differencing method (left) and filtered differencing method (right)

## Slide 11
Apparent image motion at location is approximated by following:
  is center of the patch
  the displacement of
  is rotation and scaling matrix
Rotation component is very small and we end up with scaling factor
The Affine Motion Model

## Slide 12
Contour Description
  Thresholding the spatial image gradient
Initial object description
    Finding a convex polygon enclosing all the sample points of the location that passed test for grayvalue boundaries and motion areas
Snakes (Spline approximation to contours)
  Splines are defined by control points ( shape estimation becomes quite easy)
  Cubic spline approximation of the extracted convex polygon
  Using 12 control points to approximate the polygon contour by 12 segments (spans)
Contour Extraction & Shape Estimation

## Slide 13
Figure 5: a) An image section with moving car b) the moving object mask
c) image location with well defined spatial gradient and temporal derivative
d) the convex polygon e) final description by cubic spline segments

## Slide 14
Recursive Shape and Motion Estimation
Following Vectors are defined
  They represent state vectors of vertices and state vectors of affine motions
We have (1)
  With denotes center of all n control vertices.
We can put equation (1) into matrix form

## Slide 15
Affine motion parameters
  We simply have
    )
  Measurement vector
    )
Kalman equations are used to update states with related covariance matrices
Recursive Shape and Motion Estimation

## Slide 16
Initialization
  Initial values for is derived by discrete time derivatives of the object center locations
  data association between frames is found by largest overlapping region of two patches (simple nearest neighborhood)
Recursive Shape and Motion Estimation

## Slide 17
Tracking Procedure
  Look for new blob labels that do not significantly overlap with the contour of an object already to be tracked
  Analyze all new found labels
  Move a object after the second appearance from the initialization list into the tracking list
  Analyze all objects in the tracking list by handling different occlusion cases
Recursive Shape and Motion Estimation

## Slide 18
Any contour distortion will generate an artificial shifts
  Occlusion reasoning step
we have to analyze the objects in an order according to their depth (distance to the camera)
  The depth ordered objects define the order in which objects are able to occlude each other
Occlusion Reasoning

## Slide 19
We assume that the z-axis of the camera is parallel to ground plane,
  is the height at which the camera is mounted above the road
Image coordinates for an object moving on the ground
Camera has an inclination angel toward the ground plane
  Camera coordinates
  World coordinates
Occlusion Reasoning

## Slide 20
Ground plane is plane
Y component of the image coordinate
  with
  ( )
So, depth ordering of the object can be obtained by simply considering their y coordinate in the image

## Slide 21
Occlusion reasoning procedure
  Sort the objects in the tracking list by their y coordinate of the center of the predicted contour
  Look for overlapping regions of the predicted contours and decide in the case of an overlapping region-according to the y-position –if the object is occluded or if the object occludes another object
  Analyze all objects in the tracking list by handling the different occlusion cases
Occlusion Reasoning

## Slide 22
If object under investigation occludes another object, we remove the image area associated of the other object in the contour estimation task but keep the overlapping part; in the case of getting occluded, we remove the area associated of the other object and used the predicted contour as new measurement to update the motion and shape parameters

## Slide 23
Performing experiments on two image sequences
  for first derivative of Gaussian for convolution; Thresholding for the spatial and temporal derivatives inside an image patch and
  For the affine motion estimation we set:
Results with real world Traffic Scenes

## Slide 24
For shape estimation, we assume independent measurement noise with pixel for each vertex and a start covariance with
As process noise for each vertex we set w=0.001, number of control vertices is always 12
A sequence of 84 frames recorded from an overpass of divided 4 lane freeway
Results with real world Traffic Scenes

## Slide 27
Machine vision based system for robust detection and tracking of multiple vehicles was designed
Reliable trajectories of vehicles are obtained by considering an occlusion reasoning
Convex contours are used to describe objects (snakes)
Tracker is based on two simple kalman filter for estimating the affine motion parameters and the control points of the closed spline contour
Conclusion

## Slide 28: Thank You
QUESTIONS?

## Slide 29: Introduction
Multi target tracking requires data association
Three approaches data association
  Heuristic
    Simple rule or priori knowledge
  Probabilistic non-Bayesian
    Hypothesis testing or likelihood function
  Probabilistic Bayesian
    Conditional probabilities